## Slide 1: Basic Concepts of Sequential Circuits
Section 4.1-4.3
Lecture 01

## Slide 2: Definitions of Sequential Circuit
(Section 4-1)

## Slide 3: What is a sequential circuit
Sequential Circuit:
  a digital circuit with storage element to memorize current state
  Figure 4-1:
the counter part -- Combinational Circuit
  a digital circuit without storage element

## Slide 4: Example 1: combinational circuit
turn-on the RED LED when both of the two buttons pressed
turn-on the Green LED when at least one the two buttons pressed
turn-off the two LEDs when no buttons pressed
combinational
circuit
A
B
R
G

## Slide 5: Example 1: combinational circuit
turn-on the RED light when both the two buttons pressed
turn-on the Green light when one of the two buttons pressed
none of the LED ON when you release the buttons
there is no memory in this circuit

## Slide 6: Example 2: sequential circuit
turn ON/OFF the LED by press button A
  1st hit: ON
  2nd hit: OFF
  3rd hit: ON
  4th hit: OFF
  ...
sequential
circuit
A
R

## Slide 7: Example 2: sequential circuit
the LED may keep ON after you release the button

## Slide 8: Example 2: sequential circuit
the LED may keep ON after you release the button
storage element (D flip-flop) to memorize the state: ON/OFF

## Slide 9: Example 2: sequential circuit
hit the button A to control which LED on
  1st hit: turn on R
  2nd hit: turn off R
  3rd hit: turn on R again
  ...
to memorize state ON/OFF with one D flip-flop

## Slide 10: How to distinguish combinational and sequential circuit?

## Slide 11: Storage elements
SR latches and D-latches
edge-triggered D flip-flops

## Slide 12: Storage elements
a circuit contains one of these symbols is a sequential circuit
otherwise it is a combinational circuit

## Slide 13: Example 1: combinational circuit
turn-on the RED light when one of the two buttons pressed
turn-on the Green light when both the two buttons pressed
none of the LED ON when you release the buttons
there is no memory in this circuit

## Slide 14: Example 2: sequential circuit
the LED may keep ON after you release the button

## Slide 15: Storage Element
the D flip-flop

## Slide 16: Recall: What is a sequential circuit
Sequential Circuit:
  a digital circuit with storage element to memorize current state
  Figure 4-1:
Q1: When the storage element will memorize the input?
Q2: How long the storage element will keep its memory?

## Slide 17: The D Flip-Flop
Imagine that a D flip-flop is a box of 1-bit memory
When the D flip-flop memorize the input?
  at (positive) edge trigger of the clock (clk) signal
  like a snapshot of a camera!
D
Q
in
out
clk

## Slide 18: Timing Waveform of the D Flip-Flop
D
Q
in
out
clk
in
content
Q
time
xxxxxxx
xxxxxxx
0
0
1
1
clk

## Slide 19: The D Flip-Flop
Imagine that a D flip-flop is a box of 1-bit memory
When the D flip-flop memorize the input?
  at (positive) edge trigger of the clock (clk) signal
  like a snapshot of a camera!
  unstable input signal between two clock triggers will be ignored!
D
Q
in
out
clk

## Slide 20: Timing Waveform of the D Flip-Flop
D
Q
in
out
clk
in
content
Q
time
clk

## Slide 21: Timing Waveform of the D Flip-Flop
D
Q
in
out
clk
in
content
Q
time
clk
0
0
only the last 0 before clock trigger been memorized

## Slide 22: Timing Waveform of the D Flip-Flop
D
Q
in
out
clk
in
content
Q
time
clk
0
0
only the last 0 before clock trigger been memorized
the unstable input signals ignored

## Slide 23: Timing Waveform of the D Flip-Flop
D
Q
in
out
clk
in
content
Q
time
clk
1
1
only the last 1 before clock trigger been memorized

## Slide 24: Timing Waveform of the D Flip-Flop
time
D
Q
in
out
clk
in
content
v0
v0
v1
v2
v3
v1
v2
v3
Q
v0
v1
v2
v3
clk

## Slide 25: The D Flip-Flop
the inverse of the memory content can also be retrieved
D
Q
in
X
clk
Q’
Y

## Slide 26: Timing Waveform of the D Flip-Flop
in
X
time
xxxxxxx
clk
D
Q
in
X
clk
Q’
Y
Y
xxxxxxx

## Slide 27: Timing Waveform of the D Flip-Flop
in
X
time
xxxxxxx
clk
D
Q
in
X
clk
Q’
Y
Y
xxxxxxx
0
1
1
1
1
1
1
0
0
0
0
0

## Slide 28: Timing Waveform of the D Flip-Flop
in
X
time
xxxxxxx
clk
D
Q
in
X
clk
Q’
Y
Y
xxxxxxx
0
1
1
1
1
1
1
0
0
0
0
0
at any time, Y is always the inverse of X

## Slide 29: Summary

## Slide 30: Answer these questions briefly
Q1: What is a sequential circuit?
Q2: What’s the clock signal for?
Q3: When a D flip flop will memorize it’s input?
Q4: How long a D flip flop will keep it’s memory?

## Slide 31: Skipped Part
latches
J-K flip flop
T flip-flop
Remark: only D flip-flop is available in modern IC design!

## Slide 32: Next Lecture
sequential circuit analysis
  to draw the timing waveform from a circuit diagram
Please study Section 4.4 before the class!