## Slide 1: RTL Design for Control
Section 6-10
The dash watch example
Lecture 07

## Slide 2: What is RTL design?
a quick overview

## Slide 3: What is a register
a variable in a chip
an n-bit storage device
  triggered by clock
  D flip-flop is an 1-bit register
may with various control signals (load, shift, counting, etc.)
4
4
D
Q
clock
D
Q
in
out
clk

## Slide 4: What is RTL design (1) (What’s the clock for?)
Answer: to make the circuit doing step-by-step computation
  clock signal is fed to all registers of the circuit
  to let a sequential circuit performs its task in step-by-step manner
    one step: a micro-operation (Section 7-3)
  forms a sequence of state change on flip flops
    imagine the flip flops as variables for programming
A
B
X
0010
0101
1
0111
1000
1
1001
1010
0
1111
0000
0
1100
0011
0
time
clock
registers
input
sequence of state change
clock
Figure 5-1
registers A, B, C, …
A=B+C

## Slide 5: What is RTL design
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 6: RTL Design Methodology
an overview

## Slide 7: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 8: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
Hey you, do A=B+C
A=B+C, where A, B, C are registers

## Slide 9: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
I got overflow from A=B+C, sir

## Slide 10: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 11: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 12: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 13: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 14: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 15: Design Example: Preliminary
count-up then count-down

## Slide 16: The design spec
start counting up after START button pressed
count-down when 9 reached
holds when 0 reached again
START
counter
start
0
1
1
2
9
8
0
0
time
…
…

## Slide 17: Data path design of the up/down counter

## Slide 18: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 19: Behavior spec for data path
to count up and down
  we need a 4-bit register Q
  sometimes doing Q(t+1)=Q(t)+1
  sometimes doing Q(t+1)=Q(t)-1
  sometimes holds Q(t+1)=0
two control signals E and S
  E: count enable
  S: select count-up or down
Q
E
S

## Slide 20: Behavior spec for data path
to tell 9 is reached
  signal T
  T=1 iff Q(t)=9
to tell 0 is reached
  signal Z
  Z=1 iff Q(t)=0
Q
T
Z

## Slide 21: Behavior spec for data path (FINAL)
Q
E
S
T
Z

## Slide 22: Behavior spec of control unit
the state-diagram

## Slide 23: So we begin to design the control unit
Q
E
S
T
Z

## Slide 24: Developing the state diagram
sometimes hold, count-up, and down
Q
E
S
T
Z
Hold
Up
Down
Start
Start
T
Z

## Slide 25: What we want from the state diagram
Hold
Up
Down
Start
T
Z
time
State
counter Q
Hold
0
Up
1
2
…
9
Down
8
7
…
1
0
Hold
0

## Slide 26: Developing the state diagram
state transition
Q
E
S
T
Z
Hold
Up
Down
Start
Start
T
Z
turn to count down when 9 reached

## Slide 27: Developing the state diagram
state transition
Q
E
S
T
Z
Hold
Up
Down
Start
Start
T
Z
turn to hod state when 0 reached

## Slide 28: Developing the state diagram
the orders to data path
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 29: Developing the state diagram
the orders to data path
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z
not counting

## Slide 30: Developing the state diagram
the orders to data path
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 31: Developing the state diagram
check remaining orders by yourself!
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 32: Timing diagram of the behavior specification

## Slide 33: The complete behavior spec
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 34: Status when counting up
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 35: Timing when counting up
state
(E,S)
Q
Up
(1,0)
0
Up
Up
Up
Up
(1,0)
(1,0)
(1,0)
(1,0)
1
2
3
4
time

## Slide 36: Status of switching to counting up
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 37: Timing of switching to counting up
state
(E,S)
Q
Hold
(0,X)
0
Hold
Up
Up
Up
(1,0)
(1,0)
(1,0)
(1,0)
0
1
2
3
Start
0
1
0
0
0
time

## Slide 38: Check timing for each state and transition yourself!
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 39: Circuit design of the data path

## Slide 40: The complete behavior spec
Q
E
S
T
Z
Start

## Slide 41: Up-down counter
Control signal:
  S=0: count down
  S=1: count up
Observe when Qi inversed
combinational
circuit
S

## Slide 42: Up-down counter with clean
D
D
D
D
MUX
MUX
MUX
MUX
combinational
circuit
(A=Q+1/Q-1)
S
E

## Slide 43: Complete data path circuit
up-down
counter
S
E
4
Q
==9
==0
T
Z

## Slide 44: Circuit design for control unit
realization of the state diagram

## Slide 45: Behavior spec of the control unit
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 46: Circuit design
Hold
Up
Down
Start
T
Z
00
10
11
0
0
0
X
X
0
0
0
X
0
0
1
X
X
1
0
1
0
1
0
X
0
X
1
0
1
0
1
0
X
1
X
1
1
1
1
1
1
X
X
0
1
1
1
1
1
1
X
X
1
0
0
0
X
0
1
X
X
X
0
0
0
X
Start
T
Z
E
S
2
A
2
D
combinational
circuit
start
T
Z
E
S

## Slide 47: Circuit design
Hold
Up
Down
Start
T
Z
00
10
11
0
0
0
X
X
0
0
0
X
0
0
1
X
X
1
0
1
0
1
0
X
0
X
1
0
1
0
1
0
X
1
X
1
1
1
1
1
1
X
X
0
1
1
1
1
1
1
X
X
1
0
0
0
X
0
1
X
X
X
0
0
0
X
Start
T
Z
E
S
2
A
2
D
combinational
circuit
start
T
Z
E
S
You need an EDA tool to
help you simplify the circuit

## Slide 48: The complete circuit
Q
E
S
T
Z
Start

## Slide 49: The Dash Watch Example
Example 6-3 of the textbook

## Slide 50: The Spec
start counting when “START” button pressed
  refresh every 0.01 second
  00.00 -> 00.01 -> 00.02 ->…00.99 -> 01.00 ->…
stop counting and holds current time when “STOP” button pressed
reset time to zero when “reset” button pressed
CSS: compare-and-store
  store the fastest value in internal storage
  e.g. 10.02 will replace 11.23
(Figure 6-25, Section 6-10)

## Slide 51: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 52: Step-by-step flow-chart for the dash watch
corresponding to a state-diagram for hardware implementation

## Slide 53: Registers/Counters we have
TM: time-value
  00:00 -> 00:01 -> 00:02 ->…
  the stopwatch of your lab
  4-digit BCD counter
SD: stored data
  the fastest time till now
  SD=(TM<SD)? TM: SD when “CSS” pressed
TM
SD

## Slide 54: Step-by-step flow-chart
a hardware algorithm represented as state-diagram

## Slide 55: Step-by-step flow-chart
a hardware algorithm represented as state-diagram
one step in one cycle

## Slide 56: Step-by-step flow-chart
a hardware algorithm represented as state-diagram
one-step micro-operation in one cycle

## Slide 57: Step-by-step flow-chart
Let’s trace the hardware algorithm

## Slide 58: Step-by-step flow-chart
the initial status
SD: Stored Data
  the internal storage for the fastest value
set SD=99.99 at initial

## Slide 59: Step-by-step flow-chart
Wait for start
TM: the Timing
  the register for the current value
set TM=00.00 until “START” pressed

## Slide 60: Step-by-step flow-chart
do counting after “START” pressed
time
state
control signals
TM
S3
do TM=TM+1
00.10
00.11
00.12
00.13
do TM=TM+1

## Slide 61: Step-by-step flow-chart
various decisions after “STOP” pressed

## Slide 62: Step-by-step flow-chart
various decisions after “STOP” pressed
wait until some button pressed

## Slide 63: Step-by-step flow-chart
various decisions after “STOP” pressed
restart counting if “START” pressed again

## Slide 64: Step-by-step flow-chart
various decisions after “STOP” pressed
TM: current time value
SD: store data (fasted till now)
compare and store
SD = min {TM, SD}

## Slide 65: Step-by-step flow-chart
various decisions after “STOP” pressed
TM: current time value
SD: store data (fasted till now)
if (TM<SD) SD=TM

## Slide 66: Step-by-step flow-chart
various decisions after “STOP” pressed
TM: current time value
SD: store data (fasted till now)
do nothing and hold SD if (TM >= SD)

## Slide 67: Step-by-step flow-chart
wait for the next “START”

## Slide 68: Step-by-step flow-chart
wait for the next “START”
re-start if “START” pressed again

## Slide 69: How to convert the “hardware algorithm” to real hardware?

## Slide 70: Mapping to RTL design framework

## Slide 71: Mapping to RTL design framework
micro-operations in data path side
we need registers TM and SD (16-bit for 4-digit time value)
TM
SD

## Slide 72: Mapping to RTL design framework
state-diagram realized in the control-unit side
use the standard method in Chap. 5

## Slide 73: Mapping to RTL design framework
control signals to inform which micro-operation to perform
TM
SD

## Slide 74: Mapping to RTL design framework
status signals to guide the state transition
TM
SD

## Slide 75: Mapping to RTL design framework
And, of course, lots of button inputs
TM
SD

## Slide 76: Now we are back to this RTL design flow
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 77: Behavior specification of the data path

## Slide 78: Registers in the datapath side
TM (time value): 16-bit counters
  composed of 4 BCD counters
  00:00 -> 00:01 ->… ->99:99
SD: (stored data) fasted time till now
  16-bit register with load enable control
TM
SD

## Slide 79: Registers in the datapath side
TM (time value): 16-bit counters
  composed of 4 BCD counters
  00:00 -> 00:01 ->… ->99:99
SD: (stored data) fasted time till now
  16-bit register with load enable control
TM
SD
SD = (TM<SD)? TM: SD;

## Slide 80: Micro-operations and control signals
RSTM, ENTM, UPDATE, LSR

## Slide 81: Micro-operations and control signals
operations on TM

## Slide 82: Micro-operations and control signals
operations on register SD

## Slide 83: Status signal back to control unit
ALTB: A LessThan B
ALTB

## Slide 84: Status signal back to control unit
SD = (TM<SD)? TM: SD;

## Slide 85: Micro-operations and control signals
all operations required by the “hardware algorithm” are defined by the micro-operations (check by yourself!)

## Slide 86: Behavior specification of the control unit
the state diagram

## Slide 87: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 88: Behavior spec of the control unit
hardware algorithm
state diagram

## Slide 89: Behavior spec of the control unit
check for the match on the hardware algorithm!

## Slide 90: Behavior spec of the control unit
check for the match on the hardware algorithm!
LSR=1, UPDATE=0

## Slide 91: Behavior spec of the control unit
check for the match on the hardware algorithm!
ENTM=1

## Slide 92: Behavior spec of the control unit
check for remaining matches by yourself!

## Slide 93: Now we finish the behavior spec of the dash watch

## Slide 94: Circuit design from behavior spec

## Slide 95: Steps of RTL design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 96: Control unit design
standard method from Chap. 4

## Slide 97: Control unit design
standard method from Chap. 4
do it yourself! (notice the timing!)
D flip-flops
combinational
circuit
LSR, RSTM,
ENTM, UPDATE,…
ALTB
START, STOP, RESET

## Slide 98: Data path design

## Slide 99: Data path design
two core registers
  TM (time value): 4-digit BCD counter
    00:00 -> 00:01 -> 00:02 ->…
  SD (stored data): 16-bit register with load enable

## Slide 100: Data path design
two core registers
  TM (time value): 4-digit BCD counter
  SD (stored data): 16-bit register with load enable

## Slide 101: Data path design
two core registers
  TM (time value): 4-digit BCD counter
  SD (stored data): 16-bit register with load enable
(Figure 6-2)

## Slide 102: Data path design
How to realize these micro-operations?

## Slide 103: Data path design
How to realize these micro-operations?
Very similar to your digital clock design!

## Slide 104: Data path design
How to realize these micro-operations?

## Slide 105: Data path design
How to realize these micro-operations?
  use multiplexer (MUX) to select between multiple inputs

## Slide 106: Data path design
How to realize these micro-operations?
  use multiplexer (MUX) to select between multiple inputs

## Slide 107: Data path design
How to realize these micro-operations?
  use multiplexer (MUX) to select between multiple inputs

## Slide 108: Data path design
realize by a combinational circuit to compare
  notice the timing!

## Slide 109: Data path design
And the part to control 7-seg display
  skipped due to our FPGA board has different configuration

## Slide 110: Put it all together

## Slide 111: The Spec
start counting when “START” button pressed
  refresh every 0.01 second
  00.00 -> 00.01 -> 00.02 ->…00.99 -> 01.00 ->…
stop counting and holds current time when “STOP” button pressed
reset time to zero when “reset” button pressed
CSS: compare-and-store
  store the fastest value in internal storage
  e.g. 10.02 will replace 11.23
(Figure 7-23, Section 7-10)

## Slide 112: (1) Step-by-step flow-chart
a hardware algorithm represented as state-diagram

## Slide 113: (2) Behavior specification

## Slide 114: (3) Circuit design

## Slide 115: Hard to imagine this circuit works, right?