## Slide 1: RTL Design for Control
integrate everything on Chap. 6
prepare for Section 6-10
Lecture 07 (Part A)

## Slide 2: What is RTL design?
a quick overview

## Slide 3: What is a register
a variable in a chip
an n-bit storage device
  triggered by clock
  D flip-flop is an 1-bit register
may with various control signals (load, shift, counting, etc.)
4
4
D
Q
clock
D
Q
in
out
clk

## Slide 4: What is RTL design (1) (What’s the clock for?)
Answer: to make the circuit doing step-by-step computation
  clock signal is fed to all registers of the circuit
  to let a sequential circuit performs its task in step-by-step manner
    one step: a micro-operation (Section 7-3)
  forms a sequence of state change on flip flops
    imagine the flip flops as variables for programming
A
B
X
0010
0101
1
0111
1000
1
1001
1010
0
1111
0000
0
1100
0011
0
time
clock
registers
input
sequence of state change
clock
Figure 5-1
registers A, B, C, …
A=B+C

## Slide 5: What is RTL design
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 6: RTL Design Methodology
an overview

## Slide 7: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 8: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
Hey you, do A=B+C
A=B+C, where A, B, C are registers

## Slide 9: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
I got overflow from A=B+C, sir

## Slide 10: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 11: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 12: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 13: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 14: Steps of RTL Design
Step 0: design the algorithm
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 15: RTL Design Example (1)
a simple counter started by a button and holds the final result

## Slide 16: The design spec
start counting after START button pressed
holds when 9 reached
START
counter
start
9
9
0
1
0
1
2
…
9
8
9
0
time

## Slide 17: Design Steps
Step 1: always starts from the general framework
Step 2: specify the behavior of each part
Step 3: design circuits from behavior specification

## Slide 18: Step 2.1
behavior specification for data path

## Slide 19: Behavior spec for data path
to do counting
  we need a 4-bit register Q to do Q=Q+1
sometimes counts and sometimes not counting
  we need a control signal K to enable/disable counting
to start counting from zero
  we need a control signal L to load Q as 0
Q
K
L

## Slide 20: Behavior spec for data path
The micro-operation:
Q
K
L

## Slide 21: Behavior spec for data path
we need to tell the commander that 9 has reached
  a status signal M to tell that Q==9
Q
K
M

## Slide 22: Behavior spec (micro-operation) for data path (FINAL)
Q
K
M
L

## Slide 23: Step 2.2
Behavior specification of control unit
(draw the state diagram)

## Slide 24: Behavior spec of control unit
So we start from here
Q
K
M
Start
L

## Slide 25: Behavior spec of control unit
sometimes we count and sometimes not count
Q
K
M
Hold
Count
Start
Start
M
L

## Slide 26: Behavior spec of control unit
sending out command for counting
Q
K
M
Start
Hold
Count
Start
M
K=0
L=0
K=1
L=0
K=1
L=1
K=0
L=0
(FINAL)
L

## Slide 27: Step 3
Circuit design from behavior spec

## Slide 28: Behavior spec of the circuit
sending out command for counting
Q
K
M
Start
L

## Slide 29: Circuit design from behavior spec
control unit: realizing a state diagram
  standard method from Chap. 4
  complete by your self!
Hold
Count
Start
M
K=0
L=0
K=1
L=0
K=1
L=1
K=0
L=0
D
combinational
circuit
Start
K
S
M
L

## Slide 30: Circuit design from behavior spec
counter
clock
4
D
4
Q
Load
Count
Q==9
M
0
K
L

## Slide 31: The complete design
Verify the timing diagram yourself!
D
combinational
circuit
Start
K
S
M
L
counter
clock
4
D
4
Q
Load
Count
Q==9
M
0
K
L

## Slide 32: Design Example 2
count-up then count-down

## Slide 33: The design spec
start counting up after START button pressed
count-down when 9 reached
holds when 0 reached again
START
counter
start
0
1
1
2
9
8
0
0
time
…
…

## Slide 34: Data path design of the up/down counter

## Slide 35: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 36: Behavior spec for data path
to count up and down
  we need a 4-bit register Q
  sometimes doing Q(t+1)=Q(t)+1
  sometimes doing Q(t+1)=Q(t)-1
  sometimes holds Q(t+1)=0
two control signals E and S
  E: count enable
  S: select count-up or down
Q
E
S

## Slide 37: Behavior spec for data path
to tell 9 is reached
  signal T
  T=1 iff Q(t)=9
to tell 0 is reached
  signal Z
  Z=1 iff Q(t)=0
Q
T
Z

## Slide 38: Behavior spec for data path (FINAL)
Q
E
S
T
Z

## Slide 39: Behavior spec of control unit
the state-diagram

## Slide 40: So we begin to design the control unit
Q
E
S
T
Z

## Slide 41: Developing the state diagram
sometimes hold, count-up, and down
Q
E
S
T
Z
Hold
Up
Down
Start
Start
T
Z

## Slide 42: What we want from the state diagram
Hold
Up
Down
Start
T
Z
time
State
counter Q
Hold
0
Up
1
2
…
9
Down
8
7
…
1
0
Hold
0

## Slide 43: Developing the state diagram
state transition
Q
E
S
T
Z
Hold
Up
Down
Start
Start
T
Z
turn to count down when 9 reached

## Slide 44: Developing the state diagram
state transition
Q
E
S
T
Z
Hold
Up
Down
Start
Start
T
Z
turn to hod state when 0 reached

## Slide 45: Developing the state diagram
the orders to data path
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 46: Developing the state diagram
the orders to data path
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z
not counting

## Slide 47: Developing the state diagram
the orders to data path
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 48: Developing the state diagram
check remaining orders by yourself!
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 49: Timing diagram of the behavior specification

## Slide 50: The complete behavior spec
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 51: Status when counting up
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 52: Timing when counting up
state
(E,S)
Q
Up
(1,0)
0
Up
Up
Up
Up
(1,0)
(1,0)
(1,0)
(1,0)
1
2
3
4
time

## Slide 53: Status of switching to counting up
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 54: Timing of switching to counting up
state
(E,S)
Q
Hold
(0,X)
0
Hold
Up
Up
Up
(1,0)
(1,0)
(1,0)
(1,0)
0
1
2
3
Start
0
1
0
0
0
time

## Slide 55: Check timing for each state and transition yourself!
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 56: Circuit design of the data path

## Slide 57: The complete behavior spec
Q
E
S
T
Z
Start

## Slide 58: Up-down counter
Control signal:
  S=0: count down
  S=1: count up
Observe when Qi inversed
combinational
circuit
S

## Slide 59: Up-down counter with clean
D
D
D
D
MUX
MUX
MUX
MUX
combinational
circuit
(A=Q+1/Q-1)
S
E

## Slide 60: Complete data path circuit
up-down
counter
S
E
4
Q
==9
==0
T
Z

## Slide 61: Circuit design for control unit
realization of the state diagram

## Slide 62: Behavior spec of the control unit
Q
E
S
T
Z
Start
Hold
Up
Down
Start
T
Z

## Slide 63: Circuit design
Hold
Up
Down
Start
T
Z
00
10
11
0
0
0
X
X
0
0
0
X
0
0
1
X
X
1
0
1
0
1
0
X
0
X
1
0
1
0
1
0
X
1
X
1
1
1
1
1
1
X
X
0
1
1
1
1
1
1
X
X
1
0
0
0
X
0
1
X
X
X
0
0
0
X
Start
T
Z
E
S
2
A
2
D
combinational
circuit
start
T
Z
E
S

## Slide 64: Circuit design
Hold
Up
Down
Start
T
Z
00
10
11
0
0
0
X
X
0
0
0
X
0
0
1
X
X
1
0
1
0
1
0
X
0
X
1
0
1
0
1
0
X
1
X
1
1
1
1
1
1
X
X
0
1
1
1
1
1
1
X
X
1
0
0
0
X
0
1
X
X
X
0
0
0
X
Start
T
Z
E
S
2
A
2
D
combinational
circuit
start
T
Z
E
S
You need an EDA tool to
help you simplify the circuit

## Slide 65: The complete circuit
Q
E
S
T
Z
Start