## Slide 1: Registers and Shift Registers
Section 6-1, 6-6
Lab 03

## Slide 2: Your Task
Basic (60 pts): 8-bit register with load enable
  Show the register content on LEDs
Bonus:
  8-bit register with bi-directional shift and parallel load (+10 pts)
  8-bit register as an accumulator (+10 pts)
  Display the register content on 7-segment display (+10 pts)
    You have to implement the decoder by yourself
(10 pts for your result report)

## Slide 3: Your Task
an 8-bit register
  the register memorize the content set by the dip switch when button pressed
  display the binary content of the register on LEDs
register
8
8
dip switch
button
LEDs
1100 0010

## Slide 4: Bonus
an 8-bit register
  the register memorize the content set by the dip switch when button pressed
  display the hex content of the register 7-seg display
register
8
8
dip switch
button
7-seg display
1100 0010

## Slide 5: Bonus
an 8-bit accumulator
  When button pressed:
    the input set by dipswitch is accumulated and displayed on 7-seg display (hex)
accumulator A
8
8
dip switch
button
7-seg display
1100 0010
D

## Slide 6: Pre-Lab Report
Paper work of your design
  The Circuit diagram of your design (hierarchical drawings are preferred)
  Expected timing waveform to describe the behavior of your design