## Slide 1: Registers
Section 6-1 & 6-6
Lecture 03

## Slide 2: About Chapter 6
title “Registers and Register Transfers”
Goal: RTL design methodology
  a standard method to design any digital IC
You should be able to design any digital electronics product after finishing this chapter!
  alarm, stop watch, CPU, etc.

## Slide 3: What is RTL design?
a quick overview

## Slide 4: What is a register
a variable in a chip
an n-bit storage device
  triggered by clock
  D flip-flop is an 1-bit register
4
4
D
Q
clock
D
Q
in
out
clk

## Slide 5: What is RTL design
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 6: Remark
Why I don’t allow you to write Verilog/VHDL code now?
  EDA tools are not as smart as you think
  You should have a hardware picture in mind while writing Verilog/VHDL code
  Writing Verilog/VHDL like C may result in incorrect/poor hardware!

## Slide 7: Coming Up
We will go into Chap. 6
Lecture 03: registers design
  Section 6.1: register with parallel load
  Section 6.6: shift registers
Lecture 04: counters design and their applications
  Section 6.6
  with your digital clock lab
Lecture 05: RTL design
  RTL: register-transfer level design
  go through whole Chap. 6

## Slide 8: Register
an n-bit box for storage

## Slide 9: What is a register?
a box capable of storing n-bit data
  n=4 in this example
D
D[0]
Q[0]
D
D[1]
Q[1]
D
D[2]
Q[2]
D
D[3]
Q[3]
clock
4
4
D
Q
clock

## Slide 10: Timing behavior of the register
D
D[0]
Q[0]
D
D[1]
Q[1]
D
D[2]
Q[2]
D
D[3]
Q[3]
clock
time
clock
Q[3:0]
D[3:0]
x
v0
v0
v1
v1
v2
v2

## Slide 11: Timing behavior of the register
D
D[0]
Q[0]
D
D[1]
Q[1]
D
D[2]
Q[2]
D
D[3]
Q[3]
clock
time
clock
Q[3:0]
D[3:0]
x
0011
0011
1010
1010
1110
1110

## Slide 12: Various types of registers we will talk about
register with load enable
shift register
rotation register
shift register with parallel load
bi-directional shift register
accumulator (not mentioned in the textbook)

## Slide 13: Register with load enable
a register that only memorize input when required

## Slide 14: Spec: register with load enable
an n-bit box that only memorizes the input when Load=1
register
4
Q
4
D
clock
Load

## Slide 15: Spec: register with load enable
an n-bit box that only memorizes the input when Load=1
register
4
Q
4
D
clock
Load
x
v0
1
time
clock
Q[3:0]
D[3:0]
Load
v0
cycle t
cycle t+1

## Slide 16: Spec: register with load enable
an n-bit box that only memorizes the input when Load=1
register
4
Q
4
D
clock
Load
x
0011
1
time
clock
Q[3:0]
D[3:0]
Load
0011
cycle t
cycle t+1

## Slide 17: Spec: register with load enable
an n-bit box that only memorizes the input when Load=1
register
4
Q
4
D
clock
Load
u
v0
0
time
clock
Q[3:0]
D[3:0]
Load
u
cycle t
cycle t+1

## Slide 18: Spec: register with load enable
an n-bit box that only memorizes the input when Load=1
register
4
Q
4
D
clock
Load
1010
0011
0
time
clock
Q[3:0]
D[3:0]
Load
1010
cycle t
cycle t+1

## Slide 19: How to design a register with load enable

## Slide 20: My Steps
draw the framework of the circuit
Observation: the transfer function for bit i
Re-draw the framework: separate part for bit i
Draw the detailed circuit for bit i from the transfer function

## Slide 21: Always start from this framework
Figure 4-1

## Slide 22: The framework
register
4
Q
4
D
clock
Load
D
D
D
D
combinational
circuit
Load
clock

## Slide 23: My Steps
draw the framework of the circuit
Observation: the transfer function for bit i
Re-draw the framework: separate part for bit i
Draw the detailed circuit for bit i from the transfer function

## Slide 24: Transfer function for a bit
x
0011
1
time
clock
Q[3:0]
D[3:0]
Load
0011
cycle t
cycle t+1

## Slide 25: Transfer function for a bit
x
0101
1
time
clock
Q[3:0]
D[3:0]
Load
0101
cycle t
cycle t+1
time
clock
Load
x
1
1
1
1
cycle t
cycle t+1

## Slide 26: Transfer function for a bit
0010
0101
0
time
clock
Q[3:0]
D[3:0]
Load
0010
cycle t
cycle t+1
time
clock
Load
0
1
0
0
0
cycle t
cycle t+1

## Slide 27: My Steps
draw the framework of the circuit
Observation: the transfer function for bit i
Re-draw the framework: separate part for bit i
Draw the detailed circuit for bit i from the transfer function

## Slide 28: The framework
D
D
D
D
Load
clock

## Slide 29: My Steps
draw the framework of the circuit
Observation: the transfer function for bit i
Re-draw the framework: separate part for bit i
Draw the detailed circuit for bit i from the transfer function

## Slide 30: The combinational part for bit i
Load
0
0
0
0
0
0
1
1
0
1
0
0
0
1
1
1
1
0
0
0
1
0
1
0
1
1
0
1
1
1
1
1
Load
Load

## Slide 31: The complete circuit
4-bit register with load enable
Figure 6-2

## Slide 32: A simple shift register

## Slide 33: Various types of registers we will talk about
register with load enable
shift register
rotation register
shift register with parallel load
bi-directional shift register
accumulator

## Slide 34: A simple shift register
a 4-bit shift register in Figure 6-9

## Slide 35: Function of the simple shift register
initial state at cycle 0
0
0
0
0
1
0000
time
clock
Q[3:0]
SI
SO
1
0

## Slide 36: Function of the simple shift register
initial state at cycle 1
0
0
0
0
1
0000
time
clock
Q[3:0]
SI
SO
1
0
1000
0
0

## Slide 37: Function of the simple shift register
initial state at cycle 2
0
0
0
1
0000
time
clock
Q[3:0]
SI
SO
1
0
1000
0
0
0100
0
0
0

## Slide 38: Function of the simple shift register
The transfer function:
1
0
0
0
0000
time
clock
Q[3:0]
SI
SO
1
0
1000
0
0
0100
0
0
0

## Slide 39: Exercise: rotation register with serial input select

## Slide 40: Various types of registers we will talk about
register with load enable
shift register
rotation register
shift register with parallel load
bi-directional shift register
accumulator

## Slide 41: The Problem
design a 4-bit register with the following function:
  SEL=0: shift right with serial input
  SEL=1: rotate right
RReg
clock
SI
SEL
4
Q
time
clock
Q[3:0]
SI
SEL

## Slide 42: The Problem
design a 4-bit register with the following function:
  SEL=0: shift right with serial input
  SEL=1: rotate right
RReg
clock
SI
SEL
4
Q
time
clock
Q[3:0]
SI
SEL
0110
1
0
1011

## Slide 43: The Problem
design a 4-bit register with the following function:
  SEL=0: shift right with serial input
  SEL=1: rotate right
RReg
clock
SI
SEL
4
Q
time
clock
Q[3:0]
SI
SEL
0110
1
1
0011

## Slide 44: Recall: the multiplexer
combinational circuit to select from multiple inputs
MUX
0
1
S
A
B
C

## Slide 45: Recall: the multiplexer
combinational circuit to select from multiple inputs
MUX
0
1
S
A
B
C
0

## Slide 46: Recall: the multiplexer
combinational circuit to select from multiple inputs
MUX
0
1
S
A
B
C
1

## Slide 47: The circuit design
MUX
SEL
SI
0
1

## Slide 48: How the circuit works?
time
clock
Q[3:0]
SI
SEL
0110
1
0
1011
0
1

## Slide 49: How the circuit works?
time
clock
Q[3:0]
SI
SEL
0110
1
1
0011
1
1

## Slide 50: Bi-directional shift register with parallel load

## Slide 51: The design spec
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI

## Slide 52: The design spec
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
xxxx
00
x
x
0101
0
0

## Slide 53: The design spec
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
xxxx
01
1
x
1011
0
1
1

## Slide 54: The design spec
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
xxxx
10
x
1
1010
1
0
1

## Slide 55: The design spec
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
1100
11
x
x
1100
1
1
1
1
0
0

## Slide 56: My Steps to derive the design
Observation: the rules to set Qi
Re-draw the circuit framework from the rules to set Qi
Logic simplification and finish the final design

## Slide 57: Recall: the multiplexer
combinational circuit to select from multiple inputs
MUX
0
1
S
A
B
C

## Slide 58: Recall: the multiplexer
combinational circuit to select from multiple inputs
MUX
0
1
S
A
B
C
0

## Slide 59: Recall: the multiplexer
combinational circuit to select from multiple inputs
MUX
0
1
S
A
B
C
1

## Slide 60: The circuit design

## Slide 61: The circuit design
00
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
xxxx
00
x
x
0101

## Slide 62: The circuit design
01
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
xxxx
01
1
x
1011

## Slide 63: The circuit design
10
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
xxxx
10
x
1
1010

## Slide 64: The circuit design
11
time
clock
Q[3:0]
D[3:0]
S[1:0]
LSI
RSI
0101
1100
00
x
x
1100