## Slide 1: CPU Design Overview
a quick overview on Chap. 8
Lecture 09 (Part A)

## Slide 2: Goal of Chapter 8
Implement a CPU
two designs presented
Figure 8-15: single-cycle CPU
Figure 8-18: multi-cycle CPU

## Slide 3: Lectures to present CPU design
Figure 8-15: single-cycle CPU
Figure 8-18: multi-cycle CPU
(Sec. 8-3, 8-4)
(Sec. 8-2)

## Slide 4: Lectures to present CPU design
Figure 8-15: single-cycle CPU
Figure 8-18: multi-cycle CPU
(Sec. 8-5, Sec. 8-6)

## Slide 5: Lectures to present CPU design
Figure 8-15: single-cycle CPU
Figure 8-18: multi-cycle CPU
(Sec. 8-7~8-8)
(Sec. 8-9)

## Slide 6: How a CPU realize a high-level language program?

## Slide 7: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
40
D
50
E
60
F
memory
CPU
PC: program counter

## Slide 8: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
610
D
50
E
60
F
memory
CPU
PC: program counter
PC

## Slide 9: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
610
D
670
E
60
F
memory
CPU
PC: program counter
PC

## Slide 10: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
9
A
20
B
30
C
610
D
670
E
60
F
memory
CPU
PC: program counter
PC

## Slide 11: How a CPU works?
follow the von Neumann model
  step by step
  one instruction per step
but decompose operations into primitive and regular ones
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 12: How a CPU works?
from hardware design perspective
the data path:

## Slide 13: How a CPU works?
registers to store variables
registers

## Slide 14: How a CPU works?
function units to perform arithmetic operations (+, -, &, |, ~, ^, <<, >>)
function units

## Slide 15: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 16: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 17: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 18: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 19: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 20: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 21: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 22: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 23: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 24: Binary code representation of an assembly program
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
0100 01 0001011
0100 10 0000011
0110 01 10 11 000
1100 11 0100110
machine code in memory

## Slide 25: Instruction Set Architecture
the part that a programmer should know
  registers visible by the programmer
  operations supported (+, -, *, /, etc.)
…more will be discussed in Computer Architecture Course…

## Slide 26: Relate RTL Design Methodology to CPU Design

## Slide 27: How to design a CPU
Step 0: define the “assembly instructions” of the CPU
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
Just apply the general
RTL design method!

## Slide 28: RTL design for CPU
Figure 8-18: multi-cycle CPU
data path: a generic arithmetic unit

## Slide 29: RTL design for CPU
Figure 8-18: multi-cycle CPU
memory
instruction
address
instruction
control unit: send required control
signals to realize an instruction
control signals