## Slide 1: Assembly Programming
to define the instruction set of our sample CPU
Lecture 11

## Slide 2: Today’s Goal
What CPU you are going to implement
  the instruction set architecture
  Section 8.7

## Slide 3
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
instruction
(e.g. ADD R1, R2, R3)
control signals generated
for an instruction
to instruct the data path to perform
required operations for an instruction

## Slide 4: How a CPU realize a high-level language program?

## Slide 5: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
40
D
50
E
60
F
memory
CPU
PC: program counter

## Slide 6: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
610
D
50
E
60
F
memory
CPU
PC: program counter
PC

## Slide 7: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
10
A
20
B
30
C
610
D
670
E
60
F
memory
CPU
PC: program counter
PC

## Slide 8: The Von Neumann Model
D = A+B*C;
E = D+F;
A = A-1;
9
A
20
B
30
C
610
D
670
E
60
F
memory
CPU
PC: program counter
PC

## Slide 9: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 10: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 11: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 12: The assembly program to realize a C sample code
D = A+B*C;
E = D+F;
A = A-1;
load R1, A; //R1 = mem[A];
load R2, B; //R2 = mem[B];
load R3, C; //R3 = mem[C];
mult R4, R2, R3; //R4=R2*R3;
add R5, R1, R4; //R5=R1+R4;
store D, R5; //mem[D] = R5;
load R6, F; //R6 = mem[D];
add R7, R5, R6; //R7 = R5+R6;
store E, R7; //mem[E] = R7;
sub R1, R1, 1; //R1 = R1-1;
store A, R1; //mem[A] = R1;
assembly program

## Slide 13: Binary code representation of an assembly program
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
0100 01 0001011
0100 10 0000011
0110 01 10 11 000
1100 11 0100110
machine code in memory

## Slide 14: Instruction Set Architecture
the part that a programmer should know
  registers visible by the programmer
  operations supported (+, -, *, /, etc.)
…(more will be discussed in near future)…

## Slide 15: Overview of the instruction set architecture of our CPU
Q: How to realize all C programs?

## Slide 16: List of assembly instructions

## Slide 17: List of assembly instructions
general format of an instruction
semantics (meaning) of the instruction
RD: destination register
RA,RB: the two source registers
Example:
ADD R1, R2,R3
Meaning:
R1 = R2+R3

## Slide 18: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?

## Slide 19: Arithmetic Instructions

## Slide 20: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?

## Slide 21: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
Example: ADD R1, R2,R3
  R1=R2+R3

## Slide 22: Load/Store Instructions
To access data memory

## Slide 23: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?

## Slide 24: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
Example: LD R1, R2
  to load memory data
  R1 = mem[R2]
R1
100
R2
…
CPU
20
30
15
1000
300
…
…
0
1
100
101
102
address
Memory

## Slide 25: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
Example: LD R1, R2
  to load memory data
  R1 = mem[R2]
15
R1
100
R2
…
CPU
20
30
15
1000
300
…
…
0
1
100
101
102
address
Memory

## Slide 26: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
Example: LD R1, R2
  to load memory data
  R1 = mem[R2]
15
R1
100
R2
…
CPU
20
30
15
1000
300
…
…
0
1
100
101
102
address
Memory

## Slide 27: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
Example: ST R2, R1
  to store memory data
  mem[R2] = R1
40
R1
100
R2
…
CPU
20
30
15
1000
300
…
…
0
1
100
101
102
address
Memory

## Slide 28: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
Example: ST R2, R1
  to store memory data
  mem[R2] = R1
40
R1
100
R2
…
CPU
20
30
40
1000
300
…
…
0
1
100
101
102
address
Memory

## Slide 29: Realizing memory load instruction
LD R1, R2 //R1=mem[R2]

## Slide 30: Data path to realize a memory load
data memory is here!
address
data read from memory

## Slide 31: What is memory
a chip storing an array
  address: the index to the array
  data: content of elements of the array
100
0
20
1
50
2
…
18
50
77
51
64
52
0
127
…
address
MW
n
address
n
read_data
n
write_data

## Slide 32: What is memory
a chip storing an array
  address: the index to the array
  data: content of elements of the array
100
0
20
1
50
2
…
18
50
77
51
64
52
0
127
…
address
MW
n
address
n
read_data
n
write_data
to distinguish read/write

## Slide 33: What is memory
Read from memory
  the “load” instruction
100
0
20
1
50
2
…
18
50
77
51
64
52
0
127
…
address
MW
n
address
n
read_data
n
write_data
0
51
77

## Slide 34: What is memory
write to memory
  the “store” (ST) instruction
100
0
20
1
50
2
…
18
50
77
51
64
52
0
127
…
address
MW
n
address
n
read_data
n
write_data
1
52
300
300

## Slide 35: How to realize LD R1, R2 (R1=mem[R2])
R2
data read from memory (mem[R2])
write to R1
010
XXX
X
XXXX
1
1
001
MW=0

## Slide 36: How to realize ST R2, R1 (mem[R2]=R1)
R2
010
001
0
XXXX
X
0
XXX
R1
MW=1

## Slide 37: Branch Instructions
To control the execution flow

## Slide 38: Classifications on instructions
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?

## Slide 39: Jump (Branch) instruction
…
goto my_loc;
…
my_loc:
C = A+B;
…
Jump my_loc
…
my_loc:
load R1, A;
load R2, B;
add R3, R1, R2;
store C, R3;

## Slide 40: Jump instruction in our CPU
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?
LDI R1, 100 //R1=100
Jump R1 //goto address pointed by R1
//goto address 100

## Slide 41: Realizing if-then-else: Conditional Branch
arithmetic and logic operations
  +, -, *, /, AND, OR, …, etc.
load/store instructions
  to transfer data between CPU registers and memory
control transfer
  how to realize if-then-else, for, while, goto?

## Slide 42: Realizing if-then-else
conditional branch (conditional jump)
BRZ: branch on zero
  Example: BRZ R1, label
  if (R1==0) goto label
BRN: branch on negative
  Example: BRN R1, label
  if (R1<0) goto label

## Slide 43: Realizing if-then-else
if (a>=b) {
d = e+f;
}
else {
d = e-f;
}
m=m+1;
if (a-b<0) goto else_part;
d = e+f;
goto out_side;
else_part:
d = e-f;
out_side:
m = m+1;
SUB R0, R1, R2; //R0 = R1-R2; (R0=a-b)
BRN R0, else_part //goto else_part if R0<0
ADD R3, R4, R5; //d=e+f
JUMP out_side;
else_part:
SUB R3, R4, R5; //d=e-f
out_side:
ADD R6, R6, 1 //m=m+1

## Slide 44: Example
Write an assembly program to compute R3=|R1-R2|
  translate the following C-code to the assembly of our CPU
R3 = R1-R2;
if (R3<0) {
R3 = ~R3;
R3 = R3+1;
}
R3 = R1-R2;
if (R3<0) goto inverse;
goto exit;
inverse:
R3 = ~R3;
R3 = R3+1;
exit:
….
XOR R0, R0, R0 //R0=0
SUB R3, R1, R2
BRN R3, 2 //if(R3<0) goto PC+2 (inverse)
BRZ R0, 3 //if(R0==0) goto PC+3(exit)
NOT R3, R3
ADI R3, R3, 1
…

## Slide 45: The binary code format

## Slide 46: Binary code representation of an assembly program
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
0100 01 0001011
0100 10 0000011
0110 01 10 11 000
1100 11 0100110
machine code in memory

## Slide 47: The binary code format
(a) Register
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
Source reg-
ister B (SB)
15
9
8
6
5
3
2
0
(b) Immediate
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Operand (OP)
(c) Jump and Branch
Opcode
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Address (AD)
(Right)
Address (AD)
(Left)

## Slide 48: Instruction format 1: all operands are registers
(a) Register
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
Source reg-
ister B (SB)
15
9
8
6
5
3
2
0

## Slide 49: Instruction format 1: all operands are registers
This format supports instructions represented by:
  R1 ← R2 + R3
  R1 ← sl R2
There are three 3-bit register fields:
  DR - specifies destination register (R1 in the examples)
  SA - specifies the A source register (R2 in the first example)
  SB - specifies the B source register (R3 in the first example and R2 in the second example)
(a) Register
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
Source reg-
ister B (SB)
15
9
8
6
5
3
2
0

## Slide 50: Instruction format 1: all operands are registers
Example: ADD R1, R2,R3
  R1 ← R2 + R3
(a) Register
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
Source reg-
ister B (SB)
15
9
8
6
5
3
2
0
0000010
001
010
011
(opcode of ADD)
(R1)
(R2)
(R3)

## Slide 51: Instruction format 2
This format supports instructions described by: (LDI, ADI)
  R1 ← R2 + 3
The B Source Register field is replaced by an Operand field OP which specifies a constant.
The Operand:
  3-bit constant
  Values from 0 to 7
The constant:
  Zero-fill (on the left of) the Operand to form 16-bit constant
  16-bit representation for values 0 through 7
(b) Immediate
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Operand (OP)

## Slide 52: Instruction Format 2
Example: ADI R1, R2, 3
  R1=R2+3
(b) Immediate
Opcode
Destination
register (DR)
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Operand (OP)
opcode of ADI
R1
R2
3
1000010
001
010
011

## Slide 53: Instruction format 3
For BRN, BRZ, JMP instructions
This instruction supports changes in the sequence of instruction execution by adding an extended, 6-bit, signed 2s-complement address offset to the PC value
The 6-bit Address (AD) field replaces the DR and SB fields
  Example: Suppose that a jump is specified by the Opcode and the PC contains 45 (0…0101101) and Address contains – 12 (110100). Then the new PC value will be: 0…0101101 + (1…110100) = 0…0100001 (45 + (– 12) = 33)
The SA field is retained to permit jumps and branches on N or Z based on the contents of Source register A
(c) Jump and Branch
Opcode
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Address (AD)
(Right)
Address (AD)
(Left)

## Slide 54: Instruction format 3
Example: JUMP R3
  goto the address indicated by register R3
(c) Jump and Branch
Opcode
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Address (AD)
(Right)
Address (AD)
(Left)
opcode of Jump
xxx
R3
xxx
1110000
011
xxx
xxx

## Slide 55: Instruction format 3
Example: BRZ R2, 5
  goto current position+5 if R2=0
(c) Jump and Branch
Opcode
Source reg-
ister A (SA)
15
9
8
6
5
3
2
0
Address (AD)
(Right)
Address (AD)
(Left)
opcode of BRZ
R2
1100000
010
000
101
5

## Slide 56: Example instructions
Memory Repr
esentation
of Instruc
t
ions and
Data
D
eciimal
Ad
d
r
ess
Mem
o
r
y
C
ontents
Dec
i
mal
Op
cod
e
Other F
i
elds
Op
eration
25
00001
01 001
010
011
5 (Subtract)
DR:1,
SA:2,
SB:3
R1
¬
R2
-
R3
35
01000
00 000
100
101
32 (Store
)
S
A:4, SB:5
M[
R4]
¬
R5
45
10000
10 010
111
011
66 (Add
Im
mediate)
DR:
2
, S
A
:
7
, OP
:3
R
2
¬
R7
+ 3
55
11000
00 101
110
100
96 (Branch
on
Z
e
ro
)
AD:
44, SA:6
If R6 =
0,
PC
¬
PC
-
20
70
000
000000110
00000
Data =
1
92. Aft
e
r execution of
instruction in
35,
Data =
8
0
.

## Slide 57: Practice by Yourself
Problem 1: translate a C program to assembly
  basic arithmetic +, -
  control: for, while if-then-else
Problem 2: transform assembly prgram to machine (binary) code
Problem 3: disassemble machine code to assembly program