## Slide 1: Digit Lock
Lab 02

## Slide 2: Your Work
Design a digit lock
  initial: in Lock state
  turn to Unlock state if a key sequence matched the password
  at Unock state: turn-back to lock state if any key pressed
  Example: the passwd is: 223
1
2
3
Lock
Unlock
1
1
2
2
2
3
1
1
2
…
passwd matched, Unlock
back to lock after the key pressed

## Slide 3: Remark
Each of you will be assigned a distinct password randomly
  Check the github course page
Hint:
  the most similar design you will learn: the sequence recognizer in Section 4.5

## Slide 4: Your Pre-Lab Report
Follow the standard steps to realize your design
  draw the state diagram of your design
  draw the framework of your design and name each key signal
  derive the Boolean equations for the combinational part
D
D
combinational
circuit
X
Y
A
B

## Slide 5: Grading
Realize the digit lock: 75%
  user does not press 2+ buttons simultaneously
  due today
Fix the bug of hacking the lock by pressing all buttons together: +15%
Your final report: 10%
  turn-in the final report is a must!

## Slide 6: On realization
use “button.v” to send one-cycle pulse for each press
Quartus II steps:
  add “button.v” as a file in the project
  build a symbol over “button.v”
  use the symbol in circuit diagram
button
X1
your
design

## Slide 7: Trouble Shooting for FPGA programming

## Slide 8: Trouble Shooting for FPGA
check settings:
  Assignments->Settings->Device…
    use Active Mode with Auto detection
  Tools->Programmer->Hardware
  Check jumper on your FPGA board
The user guide for USB-Blaster: check our Wiki