## Slide 1: Registers and Shift Registers
Section 6-1, 6-6
Lab 03

## Slide 2: Your Task
(select one of the following)
an 8-bit register to memorize incoming data and display on LEDs(60 pts)
an 8-bit register to memorize incoming data and display (hex) on the 7-seg digit display (75 pts)
an 8-bit accumulator and display on the 7-seg digit display (90 pts)
(10 pts for your result report)

## Slide 3: Problem 1 (60 pts)
an 8-bit register
  the register memorize the content set by the dip switch when button pressed
  display the binary content of the register on LEDs
register
8
8
dip switch
button
LEDs
1100 0010

## Slide 4: Problem 2 (75 pts)
an 8-bit register
  the register memorize the content set by the dip switch when button pressed
  display the hex content of the register 7-seg display
register
8
8
dip switch
button
7-seg display
1100 0010

## Slide 5: Problem 3 (90 pts)
an 8-bit accumulator
  When button pressed:
    the input set by dipswitch is accumulated and displayed on 7-seg display (hex)
accumulator A
8
8
dip switch
button
7-seg display
1100 0010
D

## Slide 6: How to control the 7-seg display

## Slide 7: The 7-seg display on the board
one 8-bit bus to send the decoded signal for an 7-seg display
four En signals to indicate while 7-seg display ON
8
display
En0
En1
En2
En3

## Slide 8: 7-segment LED display
A
B
C
D
E
F
G
H
A
B
C
D
E
F
G
1
1
1
1
1
0
0

## Slide 9: The 7-seg display on the board
one 8-bit bus to send the decoded signal for an 7-seg display
four En signals to indicate while 7-seg display ON
8
display
En0
En1
En2
En3
decoded signal
for “2”
1
0
0
0
You can only send your word to an
7-seg one at a time

## Slide 10: Question
How to show 4 digits simultaneously?

## Slide 11: You have these components ready
4-to-1 MUX
4-to-2 encoder
decoder for 7-segment display
16-bit adder
Recall digital circuit course for how to design these components by yourself!

## Slide 12: Recommendation
make these components as individual modules
  register with load-enable
  shift register
modular design for easy debugging!

## Slide 13: Preparation before the Lab

## Slide 14: Pre-Lab Report
Paper work of your design
  How you derive your design
  The Circuit diagram of your design (hierarchical drawings are preferred)
  Expected timing waveform to describe the behavior of your design