## Slide 1: Term Project: CPU Design

## Slide 2: Grading Policy
Basic Stage 1 (60%): integrate data path with instruction decoder to execute all non-branch instructions
  Demo by waveform
  Instructions and memory data are sent from input ports
  Examine each instruction at least once
Basic Stage 2 (+10%) extend with branch control unit
  Show you can execute Jump, BRN, BRZ instructions
Bonus: additional instructions

## Slide 3: Instruction Enhancement (10% each)
SADD R1, R2, R3 (saturated addition)
  tmp=R2+R3
  if (tmp>127) R1=127
  if (tmp <= -128) R1=-128
ABS R1, R2 (take absolute value)
  R1=|R2|
BGE R1, 3
  if (R1>=0) goto PC+3

## Slide 4: Instruction Enhancement (10% each)
(4) LDM R1, R2 (load with post modify)
  R1=mem[R2]
  R2=R2+1
(5) ADM R1, R2, R3 (add with one operand in memory)
  R1=R2+mem[R3]
any other instructions you found in commercial CPU