## Slide 1: Computing R=|A-B| with one adder
Example of RTL design with Verilog
Lecture 08A (Appendix)

## Slide 2: What is RTL design
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 3: Goal of this lecture
let you do RTL design using Verilog
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
K: A=B+C
(if (K==1) then A=B+C;)
by EDA tool

## Slide 4: Begin of our design example
R=|A-B|

## Slide 5: Problem
Design a hardware to compute R=|A-B| using only one adder
R=|A-B|
n
A
n
B
n
R
clock
start

## Slide 6: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: design the data path
  micro-operations
  the circuit data path
Step 3: design the control unit
  finite state machine
  sequential circuit realization

## Slide 7: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start

## Slide 8: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
no operation, keep value of R

## Slide 9: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
R=A-B

## Slide 10: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
check if R<0 or not
R>=0
R<0

## Slide 11: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
R=-R

## Slide 12: The data path to compute R=|A-B|

## Slide 13: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: design the data path
  micro-operations
  the circuit data path
Step 3: design the control unit
  finite state machine
  sequential circuit realization

## Slide 14: The data path
make sure that all micro-operations can be realized!
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0

## Slide 15: Questions
write down the control signal value to realize each of the micro-operations
  R(t+1)=A+(~B)+1
  R(t+1)=(~R(t))+1
  R(t+1)=(~R(t))
you may give your own MUX encoding as you like
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0

## Slide 16: Control Signal
Realize R(t+1)=~R(t)+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
Enable
MUX
1
0
1
0
0

## Slide 17: Control Signal
Realize R(t+1)=A+(~B)+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
Enable
MUX
1
0
1
1
1

## Slide 18: Control Signal
Realize R(t+1)=R(t)
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
not loading the input
MUX
1
0
0
X
X
outcome of this part is don’t-care

## Slide 19: The control unit

## Slide 20: What’s the control unit for
hardware to send out control signals
to ask the data path to perform required micro-operations for each cycle
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
R[n-1]

## Slide 21: Behavior specification of the control unit
write down the control signals for each state
  to perform required operations
S0
S1
S2
S3
start

## Slide 22: Behavior specification of the circuit
Check the match between control signals and data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
S0
S1
S2
S3
start

## Slide 23: The timing diagram
Can you image how the circuit works?

## Slide 24: Problem (Practice by yourself)
Draw the timing diagram until the outcome R finished
A
3
B
8
start
1
0
(L, S1, S0)
state
S0
???
???
R[n-1]
???
R
???

## Slide 25: Rule of Thumb
Combinational Circuit: generate outputs at the same cycle to inputs
D Flip-Flop: A(t+1) = DA(t)
  state changes at the next cycle

## Slide 26: Timing of the control unit
control unit appears at the same cycle to the state
time
clock
state
(L,S1,S0)
S1
(1,1,1)
the same cycle
by combinational circuit

## Slide 27: Timing of the control unit
state changes at the next cycle
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2

## Slide 28: Timing of the data path
Computation at cycle t follows the control signals sent at cycle t
But the result appears on the register at cycle t+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
X
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 29: Timing of the data path
Computation at cycle t follows the control signals sent at cycle t
But the result appears on the register at cycle t+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
X
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x
combinational circuit
1
1
follows the
control signal

## Slide 30: Timing of the data path
Computation at cycle t follows the control signals sent at cycle t
But the result appears on the register at cycle t+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
X
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x
1
stored at the
next cycle

## Slide 31: Timing of the whole circuit
realize the hardware algorithm:
  do the required computation at each cycle
  and store the result at the next cycle
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 32: Timing of the whole circuit
realize the hardware algorithm:
  do the required computation at each cycle
  and store the result at the next cycle
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 33: Timing of the whole circuit
realize the hardware algorithm:
  do the required computation at each cycle
  and store the result at the next cycle
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 34: Timing of the whole circuit
state transition following the state diagram
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 35: Timing diagram of an working example
You just have to look at the hardware algorithm
A
3
B
8
start
1
0
(L, S1, S0)
state
S0
R[n-1]
R
(0,X,X)
x
x
S1
(1,1,1)
x
x
S2
-5
(0,X,X)
1
S3
(1,0,0)
-5
1
5
0
S0
(0,X,X)

## Slide 36: Verilog coding to realize the RTL design

## Slide 37: Guidelines to efficient and correct Verilog coding
Follow the RTL design method means:
  you have to get this!
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
S0
S1
S2
S3
start

## Slide 38: Guidelines to efficient and correct Verilog coding
(1) Follow the RTL design method to get
  data path in block diagram
  control unit in finite-state machine
(2) Translate your circuit in mind to Verilog with standard coding style
  block-by-block
  be aware of combinational and sequential circuit

## Slide 39: Coding the data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S
S
wire [7:0] X = (S)? A: 7'h0;
wire [7:0] Y = (S)? B: R;
wire [7:0] D = X + (~Y) + 1'b1;
reg [7:0] R;
always @(posedge clk) begin
if (reset)
R <= 7'h0;
else
R <= (L)? D: R;
end
X
Y
D

## Slide 40: Coding the data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S
S
wire [7:0] X = (S)? A: 7'h0;
wire [7:0] Y = (S)? B: R;
wire [7:0] D = X + (~Y) + 1'b1;
reg [7:0] R;
always @(posedge clk) begin
if (reset)
R <= 7'h0;
else
R <= (L)? D: R;
end
X
Y
D

## Slide 41: Coding the data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S
S
wire [7:0] X = (S)? A: 7'h0;
wire [7:0] Y = (S)? B: R;
wire [7:0] D = X + (~Y) + 1'b1;
reg [7:0] R;
always @(posedge clk) begin
if (reset)
R <= 7'h0;
else
R <= (L)? D: R;
end
X
Y
D

## Slide 42: Coding the data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S
S
wire [7:0] X = (S)? A: 7'h0;
wire [7:0] Y = (S)? B: R;
wire [7:0] D = X + (~Y) + 1'b1;
reg [7:0] R;
always @(posedge clk) begin
if (reset)
R <= 7'h0;
else
R <= (L)? D: R;
end
X
Y
D

## Slide 43: Coding the data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S
S
wire [7:0] X = (S)? A: 7'h0;
wire [7:0] Y = (S)? B: R;
wire [7:0] D = X + (~Y) + 1'b1;
reg [7:0] R;
always @(posedge clk) begin
if (reset)
R <= 7'h0;
else
R <= (L)? D: R;
end
X
Y
D

## Slide 44: Coding the control unit
the circuit framework from finite-state machine
S0
S1
S2
S3
start
D flip-flops
state [1:0]
combinational
circuit
start
{L, S1, S0}

## Slide 45: Coding the control unit
decomposition for better coding style
S0
S1
S2
S3
start
D flip-flops
state [1:0]
combinational
circuit
start
{L, S1, S0}
combinational
circuit

## Slide 46: Coding the control unit
//the state transition
always @(posedge clk) begin
if (reset)
state <= `S0;
else begin
case (state)
`S0: state <= (start)? `S1: `S0;
`S1: state <= `S2;
`S2: state <= (R7)? `S3: `S0;
`S3: state <= `S0;
endcase
end
end //the state transition
//generate control signals output
always @(*) begin
case (state)
`S0: {L, S} = 2'b0x;
`S1: {L, S} = 2'b11;
`S2: {L, S} = 2'b0x;
`S3: {L, S} = 2'b10;
endcase
end

## Slide 47: Coding the control unit
//the state transition
always @(posedge clk) begin
if (reset)
state <= `S0;
else begin
case (state)
`S0: state <= (start)? `S1: `S0;
`S1: state <= `S2;
`S2: state <= (R7)? `S3: `S0;
`S3: state <= `S0;
endcase
end
end //the state transition
//generate control signals output
always @(*) begin
case (state)
`S0: {L, S} = 2'b0x;
`S1: {L, S} = 2'b11;
`S2: {L, S} = 2'b0x;
`S3: {L, S} = 2'b10;
endcase
end
describe the state-transition rules case-by-case
standard coding style of
sequential circuit

## Slide 48: Coding the control unit
//the state transition
always @(posedge clk) begin
if (reset)
state <= `S0;
else begin
case (state)
`S0: state <= (start)? `S1: `S0;
`S1: state <= `S2;
`S2: state <= (R7)? `S3: `S0;
`S3: state <= `S0;
endcase
end
end //the state transition
//generate control signals output
always @(*) begin
case (state)
`S0: {L, S} = 2'b0x;
`S1: {L, S} = 2'b11;
`S2: {L, S} = 2'b0x;
`S3: {L, S} = 2'b10;
endcase
end
describe the rules the send-out control signals for each state
standard coding style of
combinational circuit

## Slide 49: The top-level of the hardware
connecting the control unit and the data path
using standard structural description
R[n-1]
control_unit u_control (
.start (start),
.R7 (R[7]),
.L (L),
.S (S),
.reset (reset),
.clk (clk)
);
data_path u_data_path (
.A (A),
.B (B),
.L (L),
.S (S),
.R (R),
.reset (reset),
.clk (clk)
);

## Slide 50: Still feel difficult to realize the circuit?
some suggestions

## Slide 51: Suggestion 1
Follow the RTL design methodology
Systematical analysis saves lots of your time!

## Slide 52: Suggestion 2
Modular Design
  make each of your sub-module as small as possible!
  isolated testing/debugging with each of your sub-module
  Do not try to debug a large design at a time!

## Slide 53: Suggestion 3
check timing waveform, don’t stare on your circuit/code
  trace the signal value alone your data path