## Slide 1: Counter
Lab 04

## Slide 2: The Full Spec
Display counting content (Q) on LEDs
Use dip-switches to set inputs (S and D)
Remark: 1 Hz clock generation module with be provided
counter
clock
4
D
4
Q
2
S
S1(t)
S0(t)
Q(t+1)
0
0
Q(t+1)=Q(t)
0
1
Q(t+1)=Q(t)+1
1
0
Q(t+1)=Q(t)-1
1
1
Q(t+1)=D(t)

## Slide 3: Grading Policy
Basic (70%): only hold and count-up function
Bonus:
  +10%: count-down function
  +10%: load content function
Report: 10%

## Slide 4: Pre-Lab Report
Draw the circuit diagram of the “full spec” design
Expected waveform of each functionality